## Slide 1: Choke Options
21st October 2021

## Slide 2: Requirements
Small load on electrical system (Final LSM power will be changed to only accommodate what is needed)
Simple control
Cheap
Position knowledge
Reliability

## Slide 3: Solenoid
Advantages:
Can be driven directly from LSM as is
Control is simple
Cheap
Disadvantages:
Draws 3.5A @12V
Heats up and fails quickly
No position knowledge without sensor

## Slide 4: Stepper Motor
Advantages:
Position can be known without sensor
Once in position, small/no current needed to keep it there
Could also be used as way to control lambda
Disadvantages:
Requires separate driver circuit (Could be added to LSM board)
Control algorithm is a bit more difficult

## Slide 5: Automotive Throttle Body
Advantages:
Pre-made
Simple position measuring
Motor can be driven directly from current LSM
Can be run in open-loop
Disadvantages:
Heavy
Requires more complex control
If motor reaches end stop, motor is shorted (5.5A @12V) (2.5A @5V)
Requires sensor board due to position requirements
Most expensive option (~$250)